## Slide 1: ChipImgProc Documents
Compatible with Summit.Grid 1.3.x ↑

## Slide 2
Rotate the coordinate system rather than raw images.
New gridding algorithm is built on the warp matrix.
From the pixel domain to the sub-pixel domain: x -= 0.5, y -= 0.5
Core Concepts

## Slide 3
Random Based
-- ArUco Marker Detection

## Slide 4
Detection technique for ArUco Markers.
Inputs:
  Template (templ): Template image that is used to recognized the marker.
  Mask (mask): Mask image that is used to inform the region that should be focused.
  Pyramid level (pyramid_level): The downsampling times.
  Theoretical maximum value (theor_max_val): Theoretical maximum value of the input image depth.
  Number of marker counts (nms_count_): The maximum number of counts of ArUco markers in an FOV. For example, the number of marker counts is nine for the Yz01 and Banff chip.
  Length of radius (nms_radius_): The minimum distance (pixel) between each ArUco markers.
  Input: Input images.
Outputs:
  A sorted collection of detected ArUco IDs with their matching scores and xy-positions in the corresponding images. (Use sorted ArUco IDs to filter the unreasonable ArUco IDs)
Examples:
  Summit.Grid: include/summit/app/grid/aruco_setter.hpp:81
Random Based

## Slide 5
Core concepts
  The search procedure can be classified into two stages further (pixel-level search & subpixel-level correction).
  Repeat the following pixel-level search procedure nms_count times to detect all the possible markers positions:
    Identify the most similar region to the marker frame in an FOV by using marker frame template (templ) and marker frame mask (mask), and take that region as the true marker position.
    (For some markers,) Decode the ArUco code in the marker frame found in the previous step to make sure the detected object is the ArUco marker.
    To find the position of the next marker frame more accurately, we take the current marker as the center, and exclude an user-defined circular region indicating the non-optimal matching locations.
  Pick the marker image with the highest matching score as the new template from the above procedure, and use that new template to correct the subpixel-level bias and estimate the new corresponding matching score.
  Decode all the detected ArUco markers, and store all the information (ArUco ID, matching score, detected marker position) into a sorted collection (sorted by the ArUco ID and matching score).
Random Based

## Slide 6
Random Based

## Slide 7
Fusion Array
-- General, Fluorescent Marker Detection

## Slide 8
Detection technique for general Markers.
Inputs:
  Template (templ): Template image that is used to recognized the marker.
  Mask (mask): Mask image that is used to inform the region that should be focused.
  Pyramid level (pyramid_level): The downsampling times.
  Theoretical maximum value (theor_max_val): Theoretical maximum value of the input image depth.
  Image template columns (img_templ_cols): Number of column in the template image.
  Image template rows (img_templ_rows): Number of row in the template image.
  Marker layout (mk_layout): Marker layout that is generated from the GDS spec.
  unit: Unit specifying the current working environment for input images, the algorithm, and the output results unit (PX, CELL).
  Input: Input images.
Outputs:
  A collection of detected ArUco IDs with their matching scores and xy-positions in the corresponding images.
Fusion Array

## Slide 9
Core concepts
  This algorithm first use the spec of chips to generate the candidate marker regions to narrow down the searching area.
  From each candidate marker region of the corresponding alignment marker, use the marker frame template (templ) and marker frame mask (mask) to Identify the pixel-level marker position.
  To improve the efficiency, this algorithm first detect marker positions in the downsampled images, and use those rough positions to find the accurate position in the original scale image.
  Store all the information (row ID and column ID of the alignment markers, matching score, detected marker position) into a collection.
Examples
  Summit.Grid: include/summit/app/grid/probe_ch_proc_setter.hpp: 56
Fusion Array

## Slide 10
Fusion Array

## Slide 11
Estimate Transformation Matrix

## Slide 12
Estimate the transformation matrix from the input point sets.
Inputs:
  Source (src): A collection of the marker positions found by other algorithms.
  Destination (dst): A collection of the theoretical marker positions defined according to the GDS file.
  Each member of the source set should match the corresponding member in the destination set. The order must be the same in the two point sets.
Outputs:
  A transformation matrix corresponding to the input point sets.
Concept:
  Filter the unreasonable marker position and its corresponding theoretical marker position by comparing the relationship among the points in the source set and that in the destination set.
  Estimate the transformation matrix from the remaining point sets.
Examples
  Summit.Grid: include/summit/app/grid/pipeline/chip.hpp: 832
Estimate Transformation Matrix

## Slide 13
Estimate Bias
-- Fluorescent Marker Correction

## Slide 14
Estimate the bias between the given marker positions and the true marker positions.
Inputs:
  Images (_image): Input images.
  Template (templ): Template image that is used to recognized the marker.
  Mask (mask): Mask image that is used to inform the region that should be focused.
  Hints from rescaled um (hints_rum): Theoretical marker positions (rescaled um domain) from the GDS file. These positions are used to generate the given marker positions via the transformation of the warp_mat.
  Warp matrix (warp_mat): The given transformation matrix (warp matrix) that is used to generate the given marker positions through transforming the hints_rum.
  Global search (global_search): A Boolean value specifying the searching region. When it is set to true, all the possible region will be used to search. The default value is false.
  Basic cover size (basic_cover_size): A cv::Size specifying the size of the basic cover region representing the random movement caused from the SUMMIT hardware.
  The extended ratio of the high probability cover (high_P_cover_extend_r): A ratio (relative to the templ size) specifying the cover region with the higher probability of the appearance of the marker.
Estimate Bias

## Slide 15
Inputs:
  Regulation (regulation): A Boolean value specifying the judgement for the rationality of the relative bias from the true marker position. The default value is false.
  The extended ratio of the regulation cover (regulation_cover_extend_r): A ratio (relative to the templ size) specifying the cover region that is used to judge the rationality of the relative bias from the true marker position.
Outputs:
  The bias between the given marker positions and the true marker positions and its corresponding matching score.
Examples:
  Summit.Grid: include/summit/app/grid/pipeline/fov_ag.hpp:239
Estimate Bias

## Slide 16
Core concepts
  This algorithm first uses the warp_mat and hints_rum to generate the candidate marker positions.
  For the local search, Use the basic_cover_size and the high_P_cover_extend_r to generate the local cover to narrow down the searching area for each marker.
  For the global search, compute the searching area (all possible position) for each marker.
  To find the marker position more accurately, the algorithm takes the rotated template and mask to recognize the marker position in the specified searching area whose center is the candidate marker positions.
  Since the relationship among the alignment markers would not be changed after some rotation or shifts, the bias vector from the candidate marker position to the true marker position should be the same for every alignment markers theoretically.
  The algorithm then averages all the recognize results and finds the relative bias with the highest matching score.
  To take the subpixel-level bias into account, the algorithm estimate the subpixel-level bias through the Gaussian function.
  Finally, if the regulation is set to true, this algorithm will examine the rationality of the bias. If the estimated bias is smaller than the threshold user specified, the algorithm will output all the results (bias, corresponding matching score) and update the parameters in the original warp matrix.
Estimate Bias

## Slide 17
Estimate Bias

## Slide 18
Make Statistics Matrix
-- Probe Intensity Extraction

## Slide 19
Detection technique for ArUco Markers.
Inputs:
  Input image (mat): Input fluorescent images.
  Origin (origin): The origin of the coordinate system for the algorithm operation. It is usually set to (0, 0).
  Cell width in the rescaled um (clw): The probe width in the rescaled um domain.
  Cell height in the rescaled um (clh): The probe height in the rescaled um domain.
  Cell width (includes gap) in the rescaled um (clwd): The probe width (includes an x-axis gap between two adjacent probes) in the rescaled um domain.
  Cell height (includes gap) in the rescaled um (clhd): The probe height (includes a y-axis gap between two adjacent probes) in the rescaled um domain.
  FOV (w): The FOV width in the rescaled um domain.
  FOV (h): The FOV height in the rescaled um domain.
  Small (statistics) window width in px (swin_w): The width (px domain) of the small window used to compute the statistics of the probe. It will be rounded up in the algorithm.
  Small (statistics) window height in px (swin_h): The height (px domain) of the small window used to compute the statistics of the probe. It will be rounded up in the algorithm.
Make Statistics Matrix

## Slide 20
Make Statistics Matrix
  um to pixel rate (um2px_r): The transformation rate for transforming the algorithm operating coordinate from um domain to pixel domain.
  Theoretical max value (theor_max_val): Theoretical maximum value of the input image depth.
  FOV (clwn): Number of cell (probe) in the row of an FOV.
  FOV (clhn): Number of cell (probe) in the column of an FOV.
  Warp matrix (warpmat): The given transformation matrix that is used to inform the exact probe position in the fluorescent image.
  Viewer for margin result (v_margin): Debug viewer for outputting and viewing the final intensity-extracting area in the fluorescent images.
  Viewer for masking component (v_comp): Debug viewer for outputting and viewing the masking label (component) in the fluorescent image.
  Viewer for masking (v_mask): Debug viewer for outputting and viewing the masking area in the fluorescent image.
Outputs:
  A collection of computed statistics and other information (e.g. position, raw image) for each probe.
Examples:
  ChipImgProc: include/ChipImgProc/warped_mat.hpp:139

## Slide 21
Core concepts
  This algorithm first use the following steps to generate the large warped mask to identify the real probe position in the raw fluorescent images.
    Transform the mask to simulate the real probe position and the range through the given warpmat.
    Identify the pure signal region for each probe under the convolution operation.
    Remove the polluted area for each probe to get the binarized mask.
  After that, this algorithm labels the large warped mask with the natural number.
  It then stack up all the useful information and create containers for storing the computed information for each probe.
  For each probe, this algorithm follows the procedure below to extract the desired information:
    Get the label ID from the corresponding warped mask and compute the subpixel-level information (position, ROI image, warped mask) for that probe.
    Remove the artificial influence from other probes and the interpolation bias under the subpixel-level domain.
    Use the small window to compute the desired statistics for that window.
    Take the information of some window whose intensity is the most robust as the representative of that probe.
    Store all the information for the downstream analysis and summary.
Make Statistics Matrix

## Slide 22
Make Statistics Matrix

## Slide 23
Make Statistics Matrix

## Slide 24
Make Statistics Matrix

## Slide 25
Make Statistics Matrix